## Slide 1
ParkiScan Neuroverse · Game + Digital Twin · system architecture
DATA IN
DIGITAL TWIN SERVICE · PYTHON · LOCAL
CLINICIAN AND PLAYER OUT
Synthetic health record
FHIR R4 · SNOMED CT · LOINC · every resource tagged SYNTHETIC
Dashboard inside the game
F2 anywhere · live, or an offline snapshot when the service is off
Wearable streams
Daphnet ankle, thigh, trunk IMU (real, anonymised) · simulated steps, heart rate, sleep, HRV
Dashboard in a browser
/dashboard · static copy for GitHub Pages
ParkiScan Neuroverse game
3 levels · webcam, voice, drawing, memory, reaction · seated mode · 5 languages
Twin report after Level 3
six charts for the player · session synced to the twin
One twin per patient
record + wearables + game sessions on a 15-minute grid
Levodopa PK/PD model
dopamine effect, ON / OFF state, personal parameters
Risk models and what-if
A: freeze within 3 s · B: within 2 h · alert drivers · re-simulation
Part of the ParkiScan Neuroverse game
Data source or output outside the game
All data stays on the computer
Models: A predicts a freeze within 3 s from the ankle accelerometer (real data, leave-one-subject-out). B predicts a freeze within 2 h from record, wearables and the levodopa model (synthetic cohort). Research prototype, not a medical device.